## Slide 1
BCJRFormer ASIC architecture
1
Architecture and initial FSM planning
Taimor Sabek and Haiel Bader
Notes: WHAT TO SAY
Today we want to present the hardware architecture we have developed so far for BCJRFormer. I will first show what enters and leaves the core, then walk through its five main blocks. After that, I will explain the two initial controller sketches and show which FSMs still need design work. The purpose of this meeting is to agree on the next hardware steps. We are presenting an architecture proposal, not a completed or validated chip.
SOURCES / PRESENTER REFERENCE
Project handoff: Description-9.11.txt
Architecture document: bcjrformer_asic_architecture_v5.tex

## Slide 2
The neural-network core
Our current boundary starts with prepared features from the noisy DNA reads.
2
Prepared read
features
BCJRFormer
core
Prediction scores
for each position
Padding mask
Tells the core which read slots contain padding
Window preparation and final bit decisions sit outside this core.
Notes: WHAT TO SAY
This is the boundary we are using for the first architecture. The inputs are prepared features extracted from the noisy reads and a padding mask. The mask identifies missing or padded read slots. The output is a score for each encoded position, called a logit. It is not yet the final decoded message. Window preparation and hard decisions sit outside this neural-network core. A complete storage decoder may also need a separate outer error-correction stage but we are focusing only of the transformer core in the ASIC design.
SOURCES / PRESENTER REFERENCE
https://github.com/taymor3/BCJRFormer/blob/c7cf84e218730f4583e79af6dd876b04384d33f5/bcjrformer/models/bcjrformer.py
https://arxiv.org/pdf/2511.00999, Figure 4

## Slide 3
Five main blocks
Each block has a clear role in the prediction path.
3
1
Input
embedding
2
Position +
sequence
3
Transformer
stack
4
Final
projection
5
Sequence
aggregation
Prepare each
input vector
Add position
and read identity
Combine information
across positions
Produce a score
for each token
Combine scores
across reads
The padding mask also reaches the transformer and aggregation blocks.
Notes: WHAT TO SAY
The model has five main stages. Input embedding prepares the received information for the network. Position and sequence embedding add information about where a token belongs. The transformer stack combines information across the sequence and across reads. The final projection turns each token into a prediction score. Sequence aggregation combines those scores across received copies. These are logical blocks. The number of physical arithmetic units and controllers still depends on how we share hardware.
SOURCES / PRESENTER REFERENCE
https://github.com/taymor3/BCJRFormer/blob/c7cf84e218730f4583e79af6dd876b04384d33f5/bcjrformer/models/bcjrformer.py

## Slide 4
Block 1: Input embedding
Normalizes each input vector, projects it to the model width, then normalizes it again.
4
1. Idle
2. Load token
3. First statistics
4. First normalize
5. Linear calculation
6. Second statistics
7. Second normalize
8. Write output
Initial sketch: 8 states. State count does not equal clock-cycle count.
1 Input embedding
2 Position + sequence
3 Transformer stack
4 Final projection
5 Aggregation
Notes: WHAT TO SAY
This block prepares each token for the transformer. First it measures the input vector and normalizes it. Then a learned linear calculation maps it to the model width, followed by another normalization. Our saved diagram contains eight state labels, including idle, loading, and writing. This is only the first controller sketch. A calculation state can take many cycles. We still need to define the handshake, token loop, memory timing, and arithmetic precision before turning it into RTL.
SOURCES / PRESENTER REFERENCE
BCJRFormer_Architecture (2).drawio, page 3: Input Embedding FSM
https://github.com/taymor3/BCJRFormer/blob/c7cf84e218730f4583e79af6dd876b04384d33f5/bcjrformer/models/bcjrformer.py

## Slide 5
Block 1: Python implementation
bcjrformer.py:60-64 / bcjrformer.py:73 / bcjrformer.py:79
1 Input embedding
2 Position + sequence
3 Transformer stack
4 Final projection
5 Aggregation
self.to_patch_embedding = nn.Sequential(
nn.LayerNorm(window_block_dimension),
nn.Linear(window_block_dimension, model_config.d_model),
nn.LayerNorm(model_config.d_model),
)
y = y.view(bs, y.shape[1] * y.shape[2], -1)
x = self.to_patch_embedding(y)
Python computation shown here. Hardware FSMs require a separate schedule.
5
Notes: WHAT TO SAY
The highlighted block is input embedding. These lines show the exact sequence: normalization, a linear projection, and a second normalization. The view operation prepares each token’s input shape. The final line runs the embedding on the input. Our eight-state sketch controls how hardware would perform these operations over time. The Python itself does not define eight states.
SOURCE
https://github.com/taymor3/BCJRFormer/blob/c7cf84e218730f4583e79af6dd876b04384d33f5/bcjrformer/models/bcjrformer.py#L60-L64
https://github.com/taymor3/BCJRFormer/blob/c7cf84e218730f4583e79af6dd876b04384d33f5/bcjrformer/models/bcjrformer.py#L73-L73
https://github.com/taymor3/BCJRFormer/blob/c7cf84e218730f4583e79af6dd876b04384d33f5/bcjrformer/models/bcjrformer.py#L79-L79
These are raw source excerpts. Only blank lines and common leading indentation were removed. Separate excerpts appear as separate text boxes. This is not a standalone executable program.

## Slide 6
Block 2: Position and sequence embedding
Adds P[n] and E[m], learned during training and stored with the model weights.
6
1. Idle
2. Load token
3. Read P[n]
4. Add position
5. Read E[m]
6. Add sequence
7. Write output
8. Update indices
1 Input embedding
2 Position + sequence
3 Transformer stack
4 Final projection
5 Aggregation
Inference reads the saved vectors from parameter memory; it does not train them.
Notes: undefined
P[n] and E[m] are trained parameters saved in the checkpoint as pos_embed and seq_embed.weight. Load both tables into parameter memory before inference. READ POSITION and READ SEQUENCE are table reads, while ADD POSITION and ADD SEQUENCE perform vector additions. sequence_to_embed generates indices only. Source: bcjrformer/models/bcjrformer.py, lines 40–54 and 82–91.

## Slide 7
Block 2: Python implementation
bcjrformer.py:40-41 / bcjrformer.py:82-91
1 Input embedding
2 Position + sequence
3 Transformer stack
4 Final projection
5 Aggregation
self.pos_embed = torch.nn.Parameter(torch.empty((self.n, model_config.d_model)))
self.seq_embed = nn.Embedding(self.n_sequence_max, model_config.d_model)
x = x.view(x.shape[0], -1, self.n, self.model_config.d_model)
# Add position embeddings (on a per sequence basis)
x += self.pos_embed
# [batch_size, n_seq, n, d_model] -> [batch_size, n_seq * n , d_model]
x = x.view(x.shape[0], -1, self.model_config.d_model)
# Add sequence embeddings (to distinguish between subsequences)
x += self.seq_embed(self.sequence_to_embed)
pos_embed and seq_embed.weight are trained tables. Inference reads and adds them.
7
Notes: WHAT TO SAY
We are now in position and sequence embedding. The first two lines define the learned embedding tables. In the forward pass, the model changes its view of the tokens, adds the position vector, and adds the sequence vector. The plus-equals lines are the two additions shown in our diagram. The sequence_to_embed index setup is elsewhere in the constructor. We do not need to read every line aloud.
SOURCE
https://github.com/taymor3/BCJRFormer/blob/c7cf84e218730f4583e79af6dd876b04384d33f5/bcjrformer/models/bcjrformer.py#L40-L41
https://github.com/taymor3/BCJRFormer/blob/c7cf84e218730f4583e79af6dd876b04384d33f5/bcjrformer/models/bcjrformer.py#L82-L91
These are raw source excerpts. Only blank lines and common leading indentation were removed. Separate excerpts appear as separate text boxes. This is not a standalone executable program.

## Slide 8
Current FSM status
Two controller sketches exist. The complete chip-level FSM count is still open.
18
Block | States in sketch | Current status
1. Input embedding | 8 | Initial sketch
2. Position + sequence | 8 | Initial sketch
3. Transformer stack | Not defined | Not defined
4. Final projection | Not defined | Not defined
5. Sequence aggregation | Not defined | Not defined
These are draft state counts, not cycle counts or a finalized controller partition.
Notes: WHAT TO SAY
This table is the most important status summary. We currently have two initial FSM sketches, and each has eight named states. The transformer, final projection, and aggregation controllers are not yet defined. We should not describe the whole chip as having sixteen states, because these are separate draft controllers, and more control logic will be needed. A top-level controller may coordinate the blocks. Attention and other sub-blocks may have local controllers, but their number depends on the hardware partition. Even after we choose the states, one state may take several cycles.
SOURCES / PRESENTER REFERENCE
BCJRFormer_Architecture (2).drawio, pages 3 and 4
bcjrformer_asic_architecture_v5.tex, Stage 3 and Stage 3A hardware views

## Slide 9
Next decisions with Amit
The next step is to turn the block structure into a concrete execution plan.
19
Core boundary
Confirm whether the first chip stops at BCJRFormer logits.
Hardware reuse
Decide which calculations share arithmetic and memory.
Controller design
Complete the transformer schedule, then refine all FSMs.
Notes: WHAT TO SAY
The next step is to agree on the architecture assumptions that control the FSM design. First, should our first chip stop at the BCJRFormer output scores, with preprocessing and outer decoding outside? Second, how much hardware should we reuse, especially inside attention and across transformer layers? Third, once we choose that schedule, we can finish the FSMs and estimate memory and cycle counts. In parallel, we still need to confirm a useful software checkpoint and evaluation baseline. Today I would like Amit’s feedback on whether this scope and order of work are appropriate.
SOURCES / PRESENTER REFERENCE
Description-9.11.txt, What still needs verification
Architecture proposal based on the inspected repository