## Slide 1
BCJRFormer ASIC architecture
1
Architecture and initial FSM planning
Taimor Sabek and Haiel Bader
Discussion with Amit Berman
16 September 2026
Notes: WHAT TO SAY
Today we want to present the hardware architecture we have developed so far for BCJRFormer. I will first show what enters and leaves the core, then walk through its five main blocks. After that, I will explain the two initial controller sketches and show which FSMs still need design work. The purpose of this meeting is to agree on the next hardware steps. We are presenting an architecture proposal, not a completed or validated chip.
SOURCES / PRESENTER REFERENCE
Project handoff: Description-9.11.txt
Architecture document: bcjrformer_asic_architecture_v5.tex

## Slide 2
The neural-network core
Our current boundary starts with prepared features from the noisy DNA reads.
2
Prepared read
features
BCJRFormer
core
Prediction scores
for each position
Padding mask
Tells the core which read slots contain padding
Window preparation and final bit decisions sit outside this core.
Notes: WHAT TO SAY
This is the boundary we are using for the first architecture. The inputs are prepared features extracted from the noisy reads and a padding mask. The mask identifies missing or padded read slots. The output is a score for each encoded position, called a logit. It is not yet the final decoded message. Window preparation and hard decisions sit outside this neural-network core. A complete storage decoder may also need a separate outer error-correction stage.
SOURCES / PRESENTER REFERENCE
https://github.com/taymor3/BCJRFormer/blob/c7cf84e218730f4583e79af6dd876b04384d33f5/bcjrformer/models/bcjrformer.py
https://arxiv.org/pdf/2511.00999, Figure 4

## Slide 3
Five main blocks
Each block has a clear role in the prediction path.
3
1
Input
embedding
2
Position +
sequence
3
Transformer
stack
4
Final
projection
5
Sequence
aggregation
Prepare each
input vector
Add position
and read identity
Combine information
across positions
Produce a score
for each token
Combine scores
across reads
The padding mask also reaches the transformer and aggregation blocks.
Notes: WHAT TO SAY
The model has five main stages. Input embedding prepares the received information for the network. Position and sequence embedding add information about where a token belongs. The transformer stack combines information across the sequence and across reads. The final projection turns each token into a prediction score. Sequence aggregation combines those scores across received copies. These are logical blocks. The number of physical arithmetic units and controllers still depends on how we share hardware.
SOURCES / PRESENTER REFERENCE
https://github.com/taymor3/BCJRFormer/blob/c7cf84e218730f4583e79af6dd876b04384d33f5/bcjrformer/models/bcjrformer.py

## Slide 4
Block 1: Input embedding
Normalizes each input vector, projects it to the model width, then normalizes it again.
4
1. Idle
2. Load token
3. First statistics
4. First normalize
5. Linear calculation
6. Second statistics
7. Second normalize
8. Write output
Initial sketch: 8 states. State count does not equal clock-cycle count.
Notes: WHAT TO SAY
This block prepares each token for the transformer. First it measures the input vector and normalizes it. Then a learned linear calculation maps it to the model width, followed by another normalization. Our saved diagram contains eight state labels, including idle, loading, and writing. This is only the first controller sketch. A calculation state can take many cycles. We still need to define the handshake, token loop, memory timing, and arithmetic precision before turning it into RTL.
SOURCES / PRESENTER REFERENCE
BCJRFormer_Architecture (2).drawio, page 3: Input Embedding FSM
https://github.com/taymor3/BCJRFormer/blob/c7cf84e218730f4583e79af6dd876b04384d33f5/bcjrformer/models/bcjrformer.py

## Slide 5
Block 2: Position and sequence embedding
Adds the encoded-position information and the received-read identity.
5
1. Idle
2. Load token
3. Read position
4. Add position
5. Read sequence
6. Add sequence
7. Write output
8. Update indices
Initial sketch: 8 states. State count does not equal clock-cycle count.
Notes: WHAT TO SAY
This block tells the network where each token belongs. It adds one learned vector for the encoded position and another for the received-sequence slot. The initial controller sketch also has eight states. It loads the token, reads and adds the two vectors, writes the result, and updates the indices. If more tokens remain, it returns to loading. Otherwise it returns to idle. Some operations could overlap later, so the final state count is still open.
SOURCES / PRESENTER REFERENCE
BCJRFormer_Architecture (2).drawio, page 4: Position+Sequence Embedding FSM
bcjrformer_asic_architecture_v5.tex, Stage 2 FSM

## Slide 6
Block 3: Transformer stack
A sequence of repeated layers refines the token representations.
6
Normalize +
self-attention
Add original
input
Normalize +
feed-forward
Residual
addition
Attention shares information between tokens.
The feed-forward block refines each token’s features.
Repeated layers preserve the token dimensions. Detailed FSMs are still open.
Notes: WHAT TO SAY
The transformer is the main computation block. Each layer has attention, a feed-forward calculation, normalization, and additions that preserve the earlier representation. Attention shares information between tokens. The feed-forward part improves each token individually. The same layer structure repeats, but each layer has its own learned parameters. The paper calls BCJRFormer decoder-only, while the code calls this class TransformerEncoder. There is no missing second transformer stack. We have defined the structure, but have not finalized its controller or hardware sharing. The bypass operands are the original layer input for the first addition and the first residual result for the second.
SOURCES / PRESENTER REFERENCE
https://github.com/taymor3/BCJRFormer/blob/c7cf84e218730f4583e79af6dd876b04384d33f5/bcjrformer/models/modules.py
https://arxiv.org/pdf/2511.00999, Sections III-E and IV-A

## Slide 7
Inside the attention block
Attention decides which other tokens contribute to each output.
7
Create queries,
keys and values
Compare
queries and keys
Turn scores
into weights
Combine values
using the weights
Output
projection
Values
Hardware sharing and memory access determine the eventual FSM.
Notes: WHAT TO SAY
This slide opens the attention block one level. Queries and keys let the network compare tokens and calculate relevance scores. Those scores become weights, and the weights determine how to combine the value vectors. An output projection prepares the result for the residual addition. We do not need the detailed equations for this discussion. The key hardware question is whether these calculations share an arithmetic engine. That choice, together with memory access, determines the controller states. We have not fixed an attention FSM count yet. Masking and head splitting are omitted from this simplified diagram. The attention-mask behavior remains a code-review item.
SOURCES / PRESENTER REFERENCE
https://github.com/taymor3/BCJRFormer/blob/c7cf84e218730f4583e79af6dd876b04384d33f5/bcjrformer/models/modules.py

## Slide 8
Blocks 4 and 5: Output prediction
The last stages turn token features into one score per encoded position.
8
Transformer
output
4. Final
projection
5. Sequence
aggregation
Produce one score
for each token
Average across valid reads
when multiple reads exist
Both blocks still need controller sketches and final state counts.
Notes: WHAT TO SAY
The final projection converts the transformer features into a score for each token. Sequence aggregation then combines scores belonging to the same encoded position across the received reads. In the multi-read path, the code zeros padded entries and divides the sum by the valid-read count. With one read, the model bypasses this aggregation. These operations are simpler than attention, but they still need memory control and a schedule. Neither block has a completed FSM sketch in our saved artifacts.
SOURCES / PRESENTER REFERENCE
https://github.com/taymor3/BCJRFormer/blob/c7cf84e218730f4583e79af6dd876b04384d33f5/bcjrformer/models/bcjrformer.py

## Slide 9
Current FSM status
Two controller sketches exist. The complete chip-level FSM count is still open.
9
Block | States in sketch | Current status
1. Input embedding | 8 | Initial sketch
2. Position + sequence | 8 | Initial sketch
3. Transformer stack | Not defined | Structure only
4. Final projection | Not defined | Structure only
5. Sequence aggregation | Not defined | Structure only
These are draft state counts, not cycle counts or a finalized controller partition.
Notes: WHAT TO SAY
This table is the most important status summary. We currently have two initial FSM sketches, and each has eight named states. The transformer, final projection, and aggregation controllers are not yet defined. We should not describe the whole chip as having sixteen states, because these are separate draft controllers, and more control logic will be needed. A top-level controller may coordinate the blocks. Attention and other sub-blocks may have local controllers, but their number depends on the hardware partition. Even after we choose the states, one state may take several cycles.
SOURCES / PRESENTER REFERENCE
BCJRFormer_Architecture (2).drawio, pages 3 and 4
bcjrformer_asic_architecture_v5.tex, Stage 3 and Stage 3A hardware views

## Slide 10
Next decisions with Amit
The next step is to turn the block structure into a concrete execution plan.
10
Core boundary
Confirm whether the first chip stops at BCJRFormer logits.
Hardware reuse
Decide which calculations share arithmetic and memory.
Controller design
Complete the transformer schedule, then refine all FSMs.
Notes: WHAT TO SAY
The next step is to agree on the architecture assumptions that control the FSM design. First, should our first chip stop at the BCJRFormer output scores, with preprocessing and outer decoding outside? Second, how much hardware should we reuse, especially inside attention and across transformer layers? Third, once we choose that schedule, we can finish the FSMs and estimate memory and cycle counts. In parallel, we still need to confirm a useful software checkpoint and evaluation baseline. Today I would like Amit’s feedback on whether this scope and order of work are appropriate.
SOURCES / PRESENTER REFERENCE
Description-9.11.txt, What still needs verification
Architecture proposal based on the inspected repository